## Slide 1: Integrating NVIDIA Deep Learning Accelerator (NVDLA) with RISC-V SoC on FireSim
Farzad farshchi, Qijing huang, and Heechul yun
Energy Efficient Machine Learning and Cognitive Computing (EMC2), 2019
Presenter: Constant (Sang-Soo) Park
http://esoc.hanyang.ac.kr/people/sangsoo_park/index.html
September 23, 2020
Neural Network Acceleration Study Season #3

## Slide 2: Contents of presentation
Introduction and Background
  Motivation, Background knowledge
Key contribution: LLC + Memory Model
  System-on-Chip (SoC) architecture
  Memory configuration for optimized computing performance
Performance
Conclusion and Discussion
Neural Network Acceleration Study Season #3

## Slide 3: Now is the era of NPU #1
Neural Processing Unit (NPU)
  Dedicated accelerator for inference/training neural network
  Three mainstreams (ASIC/FPGA, PIM, Neuromorphic)
Neural Network Acceleration Study Season #3
Notes: The typical approach to micro-architectural design of accelerators is to find a representative workload, extract characteristics, and tailor the micro-architecture to that workload

## Slide 4: Now is the era of NPU #2
NPU in various place in our lives
  Self-driving car: TESLA (FSD Chip)[1]
  Home appliance: Samsung, LG (Robotic vacuum, TV, etc.)[2]
  Smartphone: AI assistance (Bixby, SIRI), Signal processing
FSD Chip Block Diagram
FSD Chip Die Photo
Neural Network Acceleration Study Season #3
Notes: The typical approach to micro-architectural design of accelerators is to find a representative workload, extract characteristics, and tailor the micro-architecture to that workload

## Slide 5: Motivation of paper
Useful platform for research
  SoC platform: integration of NVDLA and MCU (RISC-V)
  Limitation
    High cost of Field programmable gate array (FPGA) (about 7k cost)
    Opensource SoC platform not support an L2 cache (limited configuration)
FireSim
Chisel
Neural Network Acceleration Study Season #3
Notes: The typical approach to micro-architectural design of accelerators is to find a representative workload, extract characteristics, and tailor the micro-architecture to that workload
400 Mbyte/s

## Slide 6: SoC platform running on FireSim
DNN accelerator being incorporated into embedded system-on-chips (SoCs)
  NVDLA (NVIDIA Deep Learning Accelerator) inside Xavier SoC platform
  SiFive’s RISC-V SoC (Rocket Chip), Freedom U540 SoC platform
  FireSim: FPGA-accelerated full-system simulator running Amazon cloud FPGAs
We believe SiFive’s integration of NVDLA is especially a useful platform for conducting research thanks to its opensource nature.
Neural Network Acceleration Study Season #3
Notes: The typical approach to micro-architectural design of accelerators is to find a representative workload, extract characteristics, and tailor the micro-architecture to that workload

## Slide 7: NVDLA (NVIDIA Deep Learning Accelerator)
Microarchitecture designed by NVIDIA for acceleration DNN
  Specifically optimized for CNN (workloads deal with images and video)
  Targeting edge devices, IoT application, and other lower-power inference designs
Neural Network Acceleration Study Season #3
Notes: The typical approach to micro-architectural design of accelerators is to find a representative workload, extract characteristics, and tailor the micro-architecture to that workload

## Slide 8: Rocket Chip (NVIDIA Deep Learning Accelerator)
Opensource RISC architecture
  Expandable instruction set architecture (ISA) for RISC processor
  Inside SSD controller, 5G modem, IoT sensor, power-management IC (PMIC)
  Implemented by chisel language
Neural Network Acceleration Study Season #3

## Slide 9: Chisel
HW description language for advanced circuit generation and design reuse
  Productive Hardware description language (HDL)
    Instance port mapping, Instance reuse
    Designer can design hardware architecture like high-level programming (Scala)
class FirFilter(bitWidth: Int, coeffs: Seq[UInt]) extends Module {
val io = IO(new Bundle {
val in = Input(UInt(bitWidth.W))
val out = Output(UInt(bitWidth.W))
})
// Create the serial-in, parallel-out shift register
val zs = Reg(Vec(coeffs.length, UInt(bitWidth.W)))
zs(0) := io.in
for (i <- 1 until coeffs.length) {
zs(i) := zs(i-1)
}
// Do the multiplies
val products = VecInit.tabulate(coeffs.length)(i => zs(i) * coeffs(i))
// Sum up the products
io.out := products.reduce(_ + _)
}
Neural Network Acceleration Study Season #3

## Slide 10: FireSim
FPGA-accelerated cycle-accurate HW simulation in cloud
  Running HW design at near-FPGA-prototype speeds on cloud FPGAs
  Obtaining cycle-accurate performance results (10~100s of MHz frequency)
  Rate for on-demand access ($1.65 per hour)
Neural Network Acceleration Study Season #3

## Slide 11: Key contribution: NVDLA integration
NVIDIA DLA (NVDLA)
  Buffer (feature map, weight), Core (MAC units), Post-processing (activation, pooling)
  AMBA* based design, Control signal (CSB), Data signal (DBB)
NVDLA integration
  TileLink based bus protocol, Bride connection (Peripheral, Front)
  Configurable LLC and Memory Model (# of sets, ways, and block size)
Neural Network Acceleration Study Season #3

## Slide 12: Performance Analysis #1
Experiment Environment
  Benchmark: YOLO v3 object detection algorithm
    66 billions operation to process 416 by 416 frame
  Be operated at lower frequency
    NVDLA block is clocked at the same frequency with the processor (FPGA)
  Baseline config
    Quad-core Rocket Core, 3.2GHz with 2048 INT8 MACs (FP <-> INT8)
Neural Network Acceleration Study Season #3

## Slide 13: Performance Analysis #2
Performance comparison
  Baseline performance of NVDLA
    67ms on NVDLA + 66ms on processor (multithreaded with OpenMP)
    Layers not supported by NVDLA are running on processor
  Titan consumes more power
    Titan Xp: 250W (TDP), 471mm2 in 16nm technology
    NVDLA: 766mW, 3.3mm2 in same technology
Neural Network Acceleration Study Season #3
24C
3840C
4C

## Slide 14: Performance Analysis #3
Effect of Last-level Cache on Performance
  Sharing LLC can be good alternative to scratchpad
    Chip area saved, less programming effort
  Varying LLC size and measuring NVDLA speedup
    Also, size of cache block (32B, 64B, and 128B)
    NVDLA is not very sensitive to LLC size
    Temporal locality in NVDLA memory accesses pattern
    Target>Minimum burst length (32B), reducing latency
  Hardware prefetching improving NVDLA performance
    Benefit of sharing LLC capturing spatial locality
Neural Network Acceleration Study Season #3
24C
3840C
4C
1.59x

## Slide 15: Performance Analysis #4
Effect of Shared Memory Interference
  NVDLA and CPU are sharing memory system
    Interference with one another when accessing the memory
    Unpredictable latency in execution of tasks running on NVDLA
  Bandwidth Write (BwWrite) benchmark to study interference caused by processor
    Co-schedule BwWrite with YOLO v3 running on NVDLA
  L1 cache (No slowdown)
    Own private data cache and WSS
    LLC and DRAM: 2.5x for co-runners
Neural Network Acceleration Study Season #3
24C
3840C
4C

## Slide 16: Conclusion
First integration platform of RISC-V + NVDLA
    NVDLA provides good acceleration performance, especially considering its low power consumption
    Larger cache block size and/or hardware prefetcher is desirable for performance
    Impact of shared memory interference between CPU and NVDLA is significant
Neural Network Acceleration Study Season #3
24C
3840C
4C

## Slide 17: Thank you
Neural Network Acceleration Study #2
Notes: 46.2/278